## Slide 1
Introduction to Reliability Engineering
e-learning course, CERN.
Introduction to
Engineering
Introduction to Reliability Engineering

## Slide 2: Learning Objectives
When you have read through and understood this material, you should be able to:
Know the definition of reliability and the factors associated with it.
Understand the concepts of Reliability, Availability and Maintainability Engineering.
Know the techniques for Reliability analysis.
Calculate the failure rate under different conditions.
Understand the failure and reliability curves as a factor of time.
Introduction to Reliability Engineering
2

## Slide 3: Reliability Definition
Generally defined as the ability of a product to perform, as expected, over certain time.
Formally defined as the probability that an item, a product, piece of equipment, or system will perform its intended function for a stated period of time under specified operating conditions.
In the simplest sense, reliability means how long an item (such as a machine) will perform its intended function without a breakdown.
Introduction to Reliability Engineering
Reliability is performance over time, probability that something will work when you want it to.
3

## Slide 4
The Reliability definition has four important elements:
  Probability (A value between 0 and 1, number of times that an event occurs (success) divided by total number trials)
e.g. probability of 0.91 means that 91 of 100 items will still be working at stated time under stated conditions
  Performance (Some criteria to define when and how product fails, which also describes what is considered to be satisfactory system operation)
  e.g. amount of beam collisions, etc
  Time (system working until time (t), used to predict probability of an item surviving without failure for a designated period of time)
  Operating conditions
  These describe the operating conditions (environmental factors, humidity, vibration, shock, temperature cycle, operational profile, etc.) that correspond to the stated product life.
e-Learning course.
Introduction to Reliability Engineering

## Slide 5: Conflicts with real world.
There are “Real World” conflicts with this definition that we need to keep in mind…
  Probability – Customers expect a probability of 1, “It Works”
  Intended Function – The product may be used in unintended ways and still be expected to work
  Under Stated Conditions – The product may be operated outside of the stated conditions and still be expected to work
  Prescribed Procedures – Customers may not have the required tools or skill level and may not follow procedures and still expect the product to work
Customers are looking for Quality over Time
e-Learning course.

## Slide 6: WHY RELIABILITY ENGINEERING?
Reliability, Availability, Maintainability, Safety and Quality are what the Customer says they are, not what the Engineers or the Designers say they are.
Companies who control the Reliability of their products can only survive in the business in future as today's consumer is more “intelligent” and product aware.
Liability for unreliable products can be very high.
Complexity of products is ever increasing and thus challenge to Reliability Engineering is also increasing.
Products are being advertised by their Reliability Ratings.
“PRIDE = Put Reliability In Daily Efforts”
Introduction to Reliability Engineering

## Slide 7: When Should Reliability Be Applied?
“From the cradle to the grave.”
i.e. The entire life cycle of the product.
e-Learning course.

## Slide 8: Basic Reliability Terms
Failure - A failure is an event when an item is not available to perform its function at specified conditions when scheduled or is not capable of performing functions to specification.
Failure Rate - The number of failures per unit of gross operating period in terms of time, events, cycles.
MTBF - Mean Time Between Failures - The average time between failure occurrences. The number of items and their operating time divided by the total number of failures. For Repairable Items
MTTF - Mean Time To Failure - The average time to failure occurrence. The number of items and their operating time divided by the total number of failures. For Repairable Items and Non-repairable Items
Hazard - The potential to cause harm. Harm including ill health and injury, damage to property, plant, products or the environment, production losses or increased liabilities.
Risk - The likelihood that a specified undesired event will occur due to the realisation of a hazard by, or during work activities or by the products and services created by work activities.
e-Learning course.

## Slide 9: Basic Reliability Terms
Maintainability - A characteristic of design, installation and operation, usually expressed as the probability that an item can be retained in, or restored to, specified operable condition within a specified interval of time when maintenance is performed in accordance with prescribed procedures.
MTTR - Mean Time To Repair - The average time to restore the item to specified conditions.
Maintenance Load - The repair time per operating time for an item.
Availability - A measure of the time that a system is actually operating versus the time that the system was planned to operate.
It is the probability that the system is operational at any random time t.
Supportability - The ability of a service supplier to maintain the Plant inbuilt reliability and to perform scheduled and unscheduled maintenance according to the Plant inbuilt maintainability with minimum costs.
e-Learning course.

## Slide 10: Reliability: an introspection
Try to formulate the answers for these questions,
What are the intended functions of your system/product?
What are the specified operating conditions ?
What is time t at which you want to estimate reliability?
What is the reliability? Do you know?
What is expected by the users?
e-Learning course.

## Slide 11: Quality, Reliability and Safety
Reliability can be considered as ”Quality over time”. Customers frequently use the terms ”quality” and ”reliability”. We need to understand what they expect.
Measurement of reliability is related to failure rates, number of failures, warranty cost etc. Thus, reliability is experienced by the customers when they use the product.
Quality Level is measured in terms of defect levels (such as ppm) when the product is received as new.
Quality and reliability both can have significant impact on Safety.
e-Learning course.

## Slide 12: Quality, Reliability and Safety
Quality defects and failures both can adversely affect safety of user, bystanders and equipment.
Some quality defects can lead to unreliable and/or unsafe product.
Some examples of how unreliabily can affect safety:
- Failure of automobile steering system, brake system, axles etc, can result in serious accidents.
- Short circuit in electrical equipment can result in a shock or death.
- Failure of safety valve in a pressure cooker, leakage of regulator of an LPG cylinder can result in an explosion.
- Poor reliability of a bridge can result in an accident and disaster
However, all failures are not safety issues and all safety issues are not due to failures.
e-Learning course.

## Slide 13
As Reliability Engineering is concerned with analyzing failures and providing feedback to design and production to prevent future failures, it is only natural that a rigorous classification of failure types must be agreed upon.
Reliability engineers usually speaks of
Failures Causes
Failure Modes
Failure Mechanisms
Reliability measurement is based on the failure rate
Some products (Non-repairable) are scrapped when they fail e.g. bulb
Other products (Repairable) are repaired e.g. washing machine.
Introduction to Reliability Engineering
A failure is an event at which the system stops to fulfill its specified function.

## Slide 14
DESIGNED TO FAIL
MANUFACTURED TO FAIL
ASSEMBLED TO FAIL
SCREENED TO FAIL
STORED TO FAIL
TRANSPORTED TO FAIL
OPERATED TO FAIL
How Do Products Really Fail
e-Learning course.
Two common types of failures:
Sudden failure (no indicators): Stress exceeds strength ….
Degradation (gradual wear out): degradation indicator such as crack growth, change of resistance, corrosion, … This is ideal for Condition-Based Maintenance
Other failures may occur
because of human errors.

## Slide 15: Failure rate over the life of a product
The failure rate is expected to vary over the life of a product – ‘Bathtub Curve’
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0
 | 60 | 35 | 25 | 24 | 24 | 24 | 24 | 23.64 | 24.05 | 35 | 60
A
C
D
B
Infant Mortality
 Useful Life 
Wearout
e-Learning course.

## Slide 16: Bathtub Curve.
A-B Early Failure / Infant mortality / Debugging / Break-in
‘Teething’ problems. Caused by design/material flaws
Eg: Joints, Welds, Contamination, Misuse, Misassembly
B-C Constant Failure / Useful life.
Lower than initial failure rate and more or less constant until end of life
C-D End of life failure / Wear out phase.
Failure rate rises again due to components reaching end of life
Eg: Corrosion, Cracking, Wear, Friction, Fatigue, Erosion, Lack of PM
e-Learning course.
16

## Slide 17: Bathtub Curve: Summary Table
Phase | Failure Rate | Possible Causes | Possible improvement actions.
Burn-in (A-B) | Decreasing (DFR) | Manufacturing defects, welding, soldering, assembly errors, part defects, poor QC, poor workmanship, etc | Better QC, Acceptance testing, Burn-in testing, screening, Highly Accelerated Stress Screening, etc.
Useful Life (B-C) | Constant (CFR) | Environment, random loads, Human errors, chance events, ’Acts of God’, etc | Excess Strength, redundancy, robust design, etc
Wear-out (C-D) | Increasing (IFR) | Fatigue, Corrosion, Aging, Friction, etc. | Derating, preventive maintenance, parts replacement, better material, improved designs, technology, etc.
e-Learning course.

## Slide 18: Managing Reliability
Reliability management is concerned with performance and conformance over the expected life of the product
A systems approach to planning for, designing in, verifying, and tracking the reliability of products throughout their life to achieve reliability goals.
Reliability of a system is often specified by the failure rate λ. 
λ = failures per time unit (in a collection of systems)
For most technical products (incl. embedded systems), λ(t) is a “bath-tub curve“:
Failure Rate
Early Life
Useful Life
Wearout
“Bathtub Curve”
e-Learning course.

## Slide 19: Reliability Characteristics
Non-Repairable Systems:
Reliability=Availability
Failure Rate
MTTF
Time to First Failure
MRL (Mean Residual or remaining Life)
Repairable Systems:
Availability …. (Function of Reliability and Maintainability)
Failure Rate and Repair Rate
MTBF
MRL (Economic Justification)
e-Learning course.

## Slide 20: Failure Rate for Repairable and Non-repairable systems
MTBF θ = Total time  Total Number of failures
Average Failure Rate  = 1  θ   θ = 1
Example:
300 cars have accumulated 45000 hours, 10 failures are observed. What is the MTBF? What is the failure rate?
Note: considering Car as repairable system, Use MTBF
MTBF = 45000/10 = 4500 hours.
Average Failure rate  = 10/45000 = 0.00022 per hour.
Five oil pumps were tested with failure hours of 45, 33, 62, 94 and 105. What is the MTTF and failure rate?
Note: considering pumps as non repairable systems, Use MTTF.
MTTF = (45+33+62+94+105) / 5 = 67.8 hours
Failure rate = 5 / (45+33+62+94+105) = 0.0147 per hour.
Note that MTTF is a reciprocal of failure rate.
e-Learning course.

## Slide 21: Example
10 components were tested. The components (not repairable) failed as follows:
Component 1,2,3,4,5 failed after 75,125, 130, 325, 525 hours. Find the failure rate and mean time till failure..
Solution:
No. of failures = 5
Total operating time = 75 + 125 + 130 + 325 + 525 + 5*525 = 3805
Failure rate  = 5 / 3805 = 0.001314
Mean time till failure = 1/
=1/0.001314
= 761.04 hours.
75
125
130
325
525
5 x 525
Introduction to Reliability Engineering
e-Learning course.

## Slide 22
Example:
50 components are tested for two weeks. 20 of them fail in this time, with an average failure time of 1.2 weeks.
What is the mean time till failure assuming a constant failure rate?
Answer:
No. Of failures = 20
Total time = 20*1.2 + 30*2 = 84 weeks
Failure rate = 20/84 = 0.238/week
Mean time till failure is estimated to be = (1/failure rate)
= 1/0.238 = 4.2 weeks.
e-Learning course.
Introduction to Reliability Engineering
22

## Slide 23
– We can take in use, known historical information from records at site to estimate the failure rates of various components.
– For example, if you had 5 hydraulic pumps in standby mode and each ran for 2000 hours in standby and 3 failed during the standby time
The failure rate during standby mode is:
Total standby hours = 5(2000 hours) = 10000 hours
Failure rate in standby mode = 3 / 10,000
= 0.0003 failures per hour
Introduction to Reliability Engineering
e-Learning course.
Calculating failure rate from historical information.

## Slide 24
FAILURE PROBABILITY DENSITY FUNCTION
FAILURE RATE FUNCTION
RELIABILITY FUNCTION
CONDITIONAL RELIABILITY FUNCTION
MEAN LIFE FUNCTION
Important Analytical Functions In Reliability Engineering
Introduction to Reliability Engineering

## Slide 25
Reliability function and failure rate
Reliability function
Probability of surviving at least till age t, i.e., that failure time is later than t
Failure rate
e-Learning course.
Introduction to Reliability Engineering
25

## Slide 26
Relationship between failure density and reliability
Relationship Between h(t), f(t), F(t) and R(t),
Remark: The failure rate h(t) is a measure of proneness to
failure as a function of age, t.
Relationship Between MTBF/MTTF and Reliability
Introduction to Reliability Engineering
e-Learning course.

## Slide 27: Example
Trial data shows that 105 items failed during a test with a total operating time of 1 million hours. (For all items i.e. both failed and passed). Also, find the reliability of the product after 1000 hours i.e. (t) =1000
The failure rate
Reliability at 1000 hours
R(1000) = 0.9
Therefore the item has a 90% chance of surviving for 1000 hours
e-Learning course.
Introduction to Reliability Engineering

## Slide 28: Example
20.2
6.1
7.1
24.4
4.2
35.3
1.8
46.7
Operating time
Down time
2.5
a) Determine the MTBF.
Solution:
Total operating time = 20.2 + 6.1 + 24.4 + 4.2 + 35.3 + 46.7
= 136.9 hours
The chart below shows operating time and breakdown time of a machine.
Introduction to Reliability Engineering

## Slide 29: Contd..
 = 4 / 136.9 = 0.02922
Therefore;
= MTBF = 1/  = 34.22 hours
b) What is the system reliability for a mission time of 20 hours?
R = e-t t = 20 hours
R= e-(0.02922)(20)
R = 55.74%
Introduction to Reliability Engineering

## Slide 30: Maintainability
Maintainability is the measure of the ability of a system or item to be retained or restored to a specified condition when maintenance is performed by qualified personnel using specified procedure and resources.
Maintabnility can be measured with Mean Time To Repair (MTTR), MTTR is average repair time and is given by
MTBMA is Mean Time Between Maintenance Actions including preventive and corrective maintenance tasks.
e-Learning course.
Introduction to Reliability Engineering

## Slide 31
OBJECTIVES OF MAINTAINABILITY
To influence design to achieve case of maintenance thus reducing maintenance time & cost.
To estimate the downtime for maintenance which, when compared with allowable downtime, determines whether redundancy is required to provide acceptable continuity of a critical function.
To estimate system availability by combining maintainability data with reliability data.
To estimate the man-hours and other resources required for performing maintenance, which are useful for determining the costs of maintenance and for maintenance planning.
Introduction to Reliability Engineering

## Slide 32
ADVANTAGES OF MAINTAINABILITY PREDICTION
It highlights areas of poor maintainability which require product improvement, modification or change of design.
It permits user to make an early assessment of whether the predicted downtime, the quality, quantity of personnel, tools and test equipment are adequate and consistent with the needs of system operational requirements.
Introduction to Reliability Engineering

## Slide 33
Maintainability is a function of the design of the system, the personnel available at the necessary skill levels, the procedures available to perform the maintenance, the test equipment available, and the environment in which the maintenance must be performed.
Maintainability is measured by Mean-Time-To-Repair (MTTTR).

MTTR =

n
i=1
i Rpi
n
i
i=1
n = number of subsystems i = Failure rate of the i th system Rpi = Repair Time for the i th unit
Introduction to Reliability Engineering

## Slide 34
Probability of Repair Within the Allowable Downtime
To calculate the probability of performing a maintenance action within an allowable time interval use:
M(t) = 1 – e - t / MTTR
Where:
t = Allowable downtime
MTTR= Expected downtime (MTTR)
Introduction to Reliability Engineering

## Slide 35
Mean-Time-To-Repair
The total corrective maintenance time divided by the total number of corrective maintenance actions during a given period of time.
Example: What is the probability of completing an action within 5 hours if the MTTR = 7 hours?
Solution: M(t) = 1 – e - t/MTTR = 1 – e5/7
= 1 - .4895 = .5105
There is approximately a 51% probability of completion.
Introduction to Reliability Engineering

## Slide 36: Availability
A measure of the degree to which an item is in the operable and committable state at the start of a mission, when the mission is called for at an unknown time.
Availability is thus defined as the probability that an item will be available when required or as the proportion of total time that an item is available for use.
The three common measures of availability are:
1. Inherent Availability (AI)
2. Achieved Availability (AA)
3. Operational Availability (Ao)
Introduction to Reliability Engineering

## Slide 37
Inherent Availability (AI)
This is the ideal state for analyzing availability. The only considerations are the MTBF and the MTTR. This measure does not take into account the time for preventive maintenance and assumes repair begins immediately upon failure of the system.
This can also be defined as steady – state availability.
The measure for inherent (potential) availability (AI) is :
AI =
Where:  = Failure rate = 1/ MTBF
 = Repair rate = 1/MTTR
Example: A system has an MTBF of 2080 hours and a MTTR of 10 Hours. What is the inherent availability of the system?
Solution:
AI =

 + 
MTBF
MTTR + MTBF
=
2080
10 + 2080
= 0.9952 or 99.52%
Introduction to Reliability Engineering
37

## Slide 38
Achieved Availability (AA)
Achieved availability is somewhat more realistic in that it takes preventive maintenance into account as well as corrective maintenance. The assumption here is that, as in AI, there is no loss of time waiting for the maintenance action to begin.
The measure for achieved (final) availability (AA) is :
A A =
Where : MTBMA is the mean time between maintenance actions both preventive and corrective.
MMT is the mean Maintenance Action Time, and MMT is further decomposed into the effects of preventive and corrective maintenance and is given as:
MTBMA
MTBMA + MMT
Introduction to Reliability Engineering

## Slide 39
F c M ct + F p M pt
F c + F p
MMT =
Where: F c is the number of corrective maintenance actions per 1000 hours
F p is the number of preventive maintenance actions per 1000 hours
M ct is the mean active time for corrective maintenance (MTTR)
M pt is the mean active time for preventive maintenance
Introduction to Reliability Engineering

## Slide 40
Example : A system has a MTBMA of 110 hours, a Fc of ½, a F p of 1, and M CT of 2 hours, and M PT of 1 hour. What is A A ?
Solution :
First calculate MMT as :
Then determine A A : A A =
(1/2) (2) + (1) (1)
1 + 1/2
= 1.33
110
110 + 1.33
= 0.988 or 98.8%
Introduction to Reliability Engineering
40

## Slide 41
Operational Availability ( A 0)
This is what generally occurs in practice.Operational availability takes into account that the maintenance response is not instantaneous, repair parts may not be in stock as well as other logistics issues.
The measure of operational (actual) availability A 0 is :
MTBMA
MTBMA + MDT
A o =
Where: MDT is mean down time.
Example : A system has a MTBMA of 168 hours and a MDT of 4 hours. What is A o ?
Solution : A o =
168
168 + 4
= 0.977 or 97.7%
Introduction to Reliability Engineering

## Slide 42
Availability for Constant Failures Rates and Mean Repair Rates
The steady – state availability was given earlier as:
A =

 + 
MTBF
MTTR + MTBF
=
The instantaneous availability, (probability) that an item will be available at time T is:
 
 +   + 
When t is large, the expression reduces to : A
+
A =
* Exp [ - (  + ) t ]

 + 
=
Introduction to Reliability Engineering

## Slide 43
Example : Given exponential failure rates and repair rates of = 5,  =3, determine the instantaneous availability at 0.2 hours:
Solution:
 
 +   + 
+
A =
exp [ - (  +  ) t ]
= .501
Example : The instantaneous unavailability for the previous example is:
Solution :
  + 
 + 
-
exp [ - (  +  ) t ] }
= 1 - {
A 
= .499
Introduction to Reliability Engineering

## Slide 44
Other configurations to consider:
Series Configuration
A
B
C
….. n
 A i

n
I = 1
i
i + i
A =
Parallel Configuration
A
B
C

n
I = 1
i
i + i
=
A = 1 -
Introduction to Reliability Engineering
44

## Slide 45
Example : Given exponential failure rates and repair times of  5,= 3, if two identical units are in series, determine the steady state (A):
Solution :
i
i + i

A =
=
3
5 + 3
(
)
3
5 + 3
(
)
9
64
= 0.14063
=
Example : If the same two units in the prior example are in parallel:
Solution:

n
i = 1
i
i + i
A = 1 -
1
1 + 1
2
2 + 2
(
(
)
)
1 -
=
5 5
8 8
(
(
)
)
= 1 -
= 1 -
25
64
= 0.6094
Introduction to Reliability Engineering
45

## Slide 46: Distribution Analysis
Distribution Analysis involves identifying the statistical distribution that the field data follows and estimates of reliability and confidence intervals based on the identified distribution
  The most basic types of Distribution Analysis involve having a complete set of data for the population or sample population and knowing all failure times (uncensored) or failure times and times at which the field study was ended (censored).
  Specialized software can be used to perform this analysis.
  You will study this topic in detail, in the RAMS training courses.
e-Learning course.

## Slide 47: Data Collection
Minimum Data Needs for each item
  Design Configuration
  When Produced
  How Many Produced
    Total Population
    Or Sample Population being studied
  When Entered Service
  When Failed
  How Many Failed
Additional Data Needed to better identify Failure Modes and Corrective/Preventive Action
  Usage Application and Environment
  How Failed – Failure Mode
  Immediate Action Taken to Repair or Replace
  Time to Repair or Replace
  Root Cause of Failure
e-Learning course.

## Slide 48: Suggested Reading. (REFERENCES).
Ireson, William Grant, Clyde F Coombs, and Richard Y Moss. Handbook of Reliability Engineering and Management. 2nd Edition. New York: McGraw Hill, 1996.
O’Connor, Patrick D T. and Kleyner, Andre. ”Practical Reliability Engineering”. Chichester: Wiley, 2012.
Grant, Eugene Lodewick, and Richard S Leavenworth. Statistical Quality Control.6th ed. McGraw-Hill series in industrial engineering and management science. New York: McGraw-Hill, 1987.
Nelson, Wayne. Accelerated Testing: Statistical Models, Test Plans, and Data Analysis. Edited by S S Wilks Samuel. Wiley Series in Probability and Mathematical Statistics. New York: John Wiley & Sons, 1990.
e-Learning course.